## Slide 1
A Control System for the TurtleSim Robot Simulator Based on Hand Gesture Recognition for Drawing Geometric Shapes
BAGDAULETKYZY AKBOTA, MARATOVA AISSULU, YERMAGAMBETOVA MADINA

## Slide 2
Problem Traditional robot control methods (keyboard, joystick, CLI) require technical skills and physical devices.
Solution A natural human-robot interface where the user draws a geometric shape in the air with their index finger, and the TurtleSim robot instantly reproduces it.
Introduction
Key Features
  Real-time hand tracking with MediaPipe
  Shape recognition using OpenCV (no machine learning training)
  Smooth drawing via ROS 2 and PD controller
  Three supported shapes: Circle, Rectangle, Triangle

## Slide 3
Existing Approaches
  Sensor gloves / markers (restrict movement)
  Static gesture recognition (limited vocabulary)
  Deep learning models (require large training datasets)
Our Contribution
  Dynamic shape drawing instead of static gestures
  No pre-training required
  Combines MediaPipe + OpenCV + ROS 2
  High accuracy (85% average) with deterministic algorithm
  Smooth trajectory reproduction using PD controller
Advantage: User simply draws what they want — no need to memorize gesture commands.
Related Works & Contribution

## Slide 4
Main Components
Hardware: Webcam + Laptop (Ubuntu 22.04 + VirtualBox)
Software Pipeline:
    Video Capture
    MediaPipe Hands (21 landmarks)
    Trajectory Accumulation + Canvas
    Shape Classification Engine
    ROS 2 Control Node (PD controller)
    TurtleSim Simulator
Communication: ROS 2 topics and services (cmd_vel, set_pen, pose)
System Architecture

## Slide 5
PD Controller for Turtle Navigation
The robot uses a Proportional-Derivative (PD) controller to follow the generated trajectory smoothly and accurately.
The controller continuously calculates two types of errors:
1. Distance Error Difference between the turtle position and target waypoint.
2. Angle Error Difference between the turtle orientation and the desired direction.
Distance Error Equation
Where:
  x_t, y_t = target waypoint
  x, y = current turtle position
This determines how far the turtle is from the target and enables real-time trajectory correction for smooth shape drawing.
PD Controller for Turtle Navigation

## Slide 6
Desired Angle Equation:
This calculates the direction toward the waypoint.
Angle Error Normalization:
This keeps the angle error between:
  −π
  +π
and prevents unstable rotations (wrap-around issue).
Desired Angle Equation & Angle Error Normalization

## Slide 7
Experimental Results
Accuracy (150 trials)
Average Times
  Hand detection: 0.03 s
  Shape classification: 0.01 s
  Drawing in TurtleSim: 3.5 – 6.0 s
Main Error Sources: hand tremor, very small/fast gestures, extreme aspect ratios.

## Slide 8
DEMO

## Slide 9
PD CONTROLLEROVERALL SYSTEM WORKFLOW
SHAPE CLASSIFICATION ALGORITHM
PD CONTROLLER

## Slide 10
Conclusion
  Successfully developed an intuitive hand-gesture control system for TurtleSim.
  Achieved 85-90% recognition accuracy under normal lighting.
  Demonstrated a complete perception–processing–action loop using only open-source tools.
  The system is simple, cost-effective, and suitable for robotics education.

## Slide 11
THANK YOU FOR ATTENTION